## Slide 1: CS 5600 Computer Systems
Lecture 8: Storage Devices

## Slide 2
Hard Drives
RAID
SSD

## Slide 3: Hard Drive Hardware

## Slide 4: A Multi-Platter Disk

## Slide 5: Addressing and Geometry
Externally, hard drives expose a large number of sectors (blocks)
  Typically 512 or 4096 bytes
  Individual sector writes are atomic
  Multiple sectors writes may be interrupted (torn write)
Drive geometry
  Sectors arranged into tracks
  A cylinder is a particular track on multiple platters
  Tracks arranged in concentric circles on platters
  A disk may have multiple, double-sided platters
Drive motor spins the platters at a constant rate
  Measured in revolutions per minute (RPM)

## Slide 6: Geometry Example
0
1
4
8
12
34
28
32
30
35
29
33
31
27
24
21
18
25
26
17
16
23
22
20
19
13
14
15
2
3
11
10
9
6
5
7
Rotation
Three tracks
One platter
Sector
Outer tracks hold more data
Read head
Seeks across the various tracks

## Slide 7: Common Disk Interfaces
ST-506  ATA  IDE  SATA
  Ancient standard
  Commands (read/write) and addresses in cylinder/head/sector format placed in device registers
  Recent versions support Logical Block Addresses (LBA)
SCSI (Small Computer Systems Interface)
  Packet based, like TCP/IP
  Device translates LBA to internal format (e.g. c/h/s)
  Transport independent
    USB drives, CD/DVD/Bluray, Firewire
    iSCSI is SCSI over TCP/IP and Ethernet

## Slide 8: Types of Delay With Disks
Three types of delay
Rotational Delay
  Time to rotate the desired sector to the read head
  Related to RPM
Seek delay
  Time to move the read head to a different track
Transfer time
  Time to read or write bytes
0
1
4
8
12
34
28
32
30
35
29
33
31
27
24
21
18
25
26
17
16
23
22
20
19
13
14
15
2
3
11
10
9
6
5
7
Rotation
Short delay
Long delay
Track skew: offset sectors so that sequential reads across tracks incorporate seek delay

## Slide 9: How To Calculate Transfer Time
 | Cheetah 15K.5 | Barracuda
Capacity | 300 GB | 1 TB
RPM | 15000 | 7200
Avg. Seek | 4 ms | 9 ms
Max Transfer | 125 MB/s | 105 MB/s
Transfer time
TI/O = Tseek + Trotation + Ttransfer
Assume we are transferring 4096 bytes
TI/O = 4 ms + 1 / (15000 RPM / 60 s/M / 1000 ms/s) / 2
+ (4096 B / 125 MB/s * 1000 ms/s / 220 MB/B)
TI/O = 4 ms + 2ms + 0.03125 ms ≈ 6 ms
Cheetah
Barracuda
TI/O = 9 ms + 1 / (7200 RPM / 60 s/M / 1000 ms/s) / 2
+ (4096 B / 105 MB/s * 1000 ms/s / 220 MB/B)
TI/O = 9 ms + 4.17 ms + 0.0372 ms ≈ 13.2 ms

## Slide 10: Sequential vs. Random Access
Rate of I/O
RI/O = transfer_size / TI/O
Access Type | Transfer Size |  | Cheetah 15K.5 | Barracuda
Random | 4096 B | TI/O | 6 ms | 13.2 ms
 |  | RI/O | 0.66 MB/s | 0.31 MB/s
Sequential | 100 MB | TI/O | 800 ms | 950 ms
 |  | RI/O | 125 MB/s | 105 MB/s
Max Transfer Rate |  |  | 125 MB/s | 105MB/s
Random I/O results in very poor disk performance!

## Slide 11: Caching
Many disks incorporate caches (track buffer)
  Small amount of RAM (8, 16, or 32 MB)
Read caching
  Reduces read delays due to seeking and rotation
Write caching
  Write back cache: drive reports that writes are complete after they have been cached
    Possibly dangerous feature. Why?
  Write through cache: drive reports that writes are complete after they have been written to disk
Today, some disks include flash memory for persistent caching (hybrid drives)

## Slide 12: Disk Scheduling
Caching helps improve disk performance
But it can’t make up for poor random access times
Key idea: if there are a queue of requests to the disk, they can be reordered to improve performance
  First come, first serve (FCFC)
  Shortest seek time first (SSTF)
  SCAN, otherwise know as the elevator algorithm
  C-SCAN, C-LOOK, etc.

## Slide 13: FCFS Scheduling
Head starts at block 53
Queue: 98, 183, 37, 122, 14, 124, 65, 67
Total movement: 640 cylinders
Lot’s of time spent seeking
Most basic scheduler, serve requests in order

## Slide 14: SSTF Scheduling
Idea: minimize seek time by always selecting the block with the shortest seek time
Total movement: 236 cylinders
Head starts at block 53
Queue: 98, 183, 37, 122, 14, 124, 65, 67
The good: SSTF is optimal, and it can be easily implemented!
The bad: SSTF is prone to starvation

## Slide 15: SCAN Example
Head sweeps across the disk servicing requests in order
Total movement: 236 cylinders
Head starts at block 53
Queue: 98, 183, 37, 122, 14, 124, 65, 67
The good: reasonable performance, no starvation
The bad: average access times are less for requests at high and low addresses

## Slide 16: C-SCAN Example
Like SCAN, but only service requests in one direction
Total movement: 382 cylinders
Head starts at block 53
Queue: 98, 183, 37, 122, 14, 124, 65, 67
The good: fairer than SCAN
The bad: worse performance than SCAN

## Slide 17: C-LOOK Example
Peek at the upcoming addresses in the queue
Head only goes as far as the last request
Total movement: 322 cylinders
Head starts at block 53
Queue: 98, 183, 37, 122, 14, 124, 65, 67

## Slide 18: Implementing Disk Scheduling
We have talked about several scheduling problems that take place in the kernel
  Process scheduling
  Page swapping
Where should disk scheduling be implemented?
  OS scheduling
    OS can implement SSTF or LOOK by ordering the queue by LBA
    However, the OS cannot account for rotation delay
  On-disk scheduling
    Disk knows the exact position of the head and platters
    Can implement more advanced schedulers (SPTF)
    But, requires specialized hardware and drivers

## Slide 19: Command Queuing
Feature where a disk stores of queue of pending read/write requests
  Called Native Command Queuing (NCQ) in SATA
Disk may reorder items in the queue to improve performance
  E.g. batch operations to close sectors/tracks
Supported by SCSI and modern SATA drives
Tagged command queuing: allows the host to place constraints on command re-ordering

## Slide 20
Hard Drives
RAID
SSD

## Slide 21: Beyond Single Disks
Hard drives are great devices
  Relatively fast, persistent storage
Shortcomings:
  How to cope with disk failure?
    Mechanical parts break over time
    Sectors may become silently corrupted
  Capacity is limited
    Managing files across multiple physical devices is cumbersome
    Can we make 10x 1 TB drives look like a 10 TB drive?

## Slide 22: Redundant Array of Inexpensive Disks
RAID: use multiple disks to create the illusion of a large, faster, more reliable disk
Externally, RAID looks like a single disk
  i.e. RAID is transparent
  Data blocks are read/written as usual
  No need for software to explicitly manage multiple disks or perform error checking/recovery
Internally, RAID is a complex computer system
  Disks managed by a dedicated CPU + software
  RAM and non-volatile memory
  Many different configuration options (RAID levels)

## Slide 23: Example RAID Controller
SATA ports
CPU
RAM
Non-volatile storage

## Slide 24: RAID 0: Striping
Key idea: present an array of disks as a single large disk
Maximize parallelism by striping data cross all N disks
0
4
8
12
Disk 0
1
5
9
13
Disk 1
2
6
10
14
Disk 2
3
7
11
15
Disk 3
Stripe
Data block = 512 bytes
Random accesses are naturally spread over all drives
Sequential accesses spread across all drives

## Slide 25: Addressing Blocks
How do you access specific data blocks?
  Disk = logical_block_number % number_of_disks
  Offset = logical_block_number / number_of_disks
Example: read block 11
  11 % 4 = Disk 3
  11 / 4 = Physical Block 2 (starting from 0)
0
4
8
12
Disk 0
1
5
9
13
Disk 1
2
6
10
14
Disk 2
3
7
11
15
Disk 3

## Slide 26: Chunk Sizing
0
4
8
12
Disk 0
1
5
9
13
Disk 1
2
6
10
14
Disk 2
3
7
11
15
Disk 3
0
1
8
9
Disk 0
2
3
10
11
Disk 1
4
5
12
13
Disk 2
6
7
14
15
Disk 3
Chunk size = 1 block
Chunk size = 2 block
Chunk size impacts array performance
  Smaller chunks  greater parallelism
  Big chunks  reduced seek times
Typical arrays use 64KB chunks

## Slide 27: Measuring RAID Performance (1)
As usual, we focus on sequential and random workloads
Assume disks in the array have sequential access time S
  10 MB transfer
  S = transfer_size / time_to_access
  10 MB / (7 ms + 3 ms + 10 MB / 50 MB/s) = 47.62 MB/s
Average seek time | 7 ms
Average rotational delay | 3 ms
Transfer rate | 50 MB/s

## Slide 28: Measuring RAID Performance (2)
As usual, we focus on sequential and random workloads
Assume disks in the array have random access time R
  10 KB transfer
  R = transfer_size / time_to_access
  10 KB / (7 ms + 3 ms + 10 KB / 50 MB/s) = 0.98 MB/s
Average seek time | 7 ms
Average rotational delay | 3 ms
Transfer rate | 50 MB/s

## Slide 29: Analysis of RAID 0
Capacity: N
  All space on all drives can be filled with data
Reliability: 0
  If any drive fails, data is permanently lost
Sequential read and write: N * S
  Full parallelization across drives
Random read and write: N * R
  Full parallelization across all drives

## Slide 30: RAID 1: Mirroring
0
1
2
3
Disk 0
0
1
2
3
Disk 1
RAID 0 offers high performance, but zero error recovery
Key idea: make two copies of all data

## Slide 31: RAID 0+1 and 1+0 Examples
0
2
4
6
Disk 0
0
2
4
6
Disk 1
1
3
5
7
Disk 2
1
3
5
7
Disk 3
0
2
4
6
Disk 0
1
3
5
7
Disk 1
0
2
4
6
Disk 2
1
3
5
7
Disk 3
Stripe
Stripe
Mirror
Mirror
Mirror
Stripe
Combines striping and mirroring
Superseded by RAID 4, 5, and 6
0+1
1+0

## Slide 32: Analysis of RAID 1 (1)
Capacity: N / 2
  Two copies of all data, thus half capacity
Reliability: 1 drive can fail, sometime more
  If you are lucky, N / 2 drives can fail without data loss
0
2
4
6
Disk 0
1
3
5
7
Disk 1
0
2
4
6
Disk 2
1
3
5
7
Disk 3

## Slide 33: Analysis of RAID 1 (2)
Sequential write: (N / 2) * S
  Two copies of all data, thus half throughput
Sequential read: (N / 2) * S
  Half of the read blocks are wasted, thus halving throughput
0
2
4
6
Disk 0
1
3
5
7
Disk 1
0
2
4
6
Disk 2
1
3
5
7
Disk 3
Each skipped block is wasted

## Slide 34: Analysis of RAID 1 (3)
Random read: N * R
  Best case scenario for RAID 1
  Reads can parallelize across all disks
Random write: (N / 2) * R
  Two copies of all data, thus half throughput
0
2
4
6
Disk 0
1
3
5
7
Disk 1
0
2
4
6
Disk 2
1
3
5
7
Disk 3

## Slide 35: The Consistent Update Problem
Mirrored writes should be atomic
  All copies are written, or none are written
However, this is difficult to guarantee
  Example: power failure
Many RAID controllers include a write-ahead log
  Battery backed, non-volatile storage of pending writes
0
2
4
6
Disk 0
1
3
5
7
Disk 1
0
2
4
6
Disk 2
1
3
5
7
Disk 3
RAID Controller
Cache

## Slide 36: Decreasing the Cost of Reliability
RAID 1 offers highly reliable data storage
But, it uses N / 2 of the array capacity
Can we achieve the same level of reliability without wasting so much capacity?
  Yes!
  Use information coding techniques to build light-weight error recovery mechanisms

## Slide 37: RAID 4: Parity Drive
0
4
8
12
Disk 0
1
5
9
13
Disk 1
2
6
10
14
Disk 2
3
7
11
15
Disk 3
P0
P1
P2
P3
Disk 4
Disk 0 | Disk 1 | Disk 2 | Disk 3 | Disk 4
0 | 0 | 1 | 1 | 0 ^ 0 ^ 1 ^ 1 = 0
0 | 1 | 0 | 0 | 0 ^ 1 ^ 0 ^ 0 = 1
1 | 1 | 1 | 1 | 1 ^ 1 ^ 1 ^ 1 = 0
0 | 1 | 1 | 1 | 0 ^ 1 ^ 1 ^ 1 = 1
Disk N only stores parity information for the other N-1 disks
Parity calculated using XOR

## Slide 38: Updating Parity on Write
How is parity updated when blocks are written?
Additive parity
Subtractive parity
Disk 0 | Disk 1 | Disk 2 | Disk 3 | Disk 4
0 | 0 | 1 | 1 | 0 ^ 0 ^ 1 ^ 1 = 0
0
0 ^ 0 ^ 0 ^ 1 = 1
Read other blocks
Update parity block
Disk 0 | Disk 1 | Disk 2 | Disk 3 | Disk 4
0 | 0 | 1 | 1 | 0 ^ 0 ^ 1 ^ 1 = 0
0
1
Pnew = Cold ^ Cnew ^ Pold

## Slide 39: Random Writes and RAID 4
0
4
8
12
Disk 0
1
5
9
13
Disk 1
2
6
10
14
Disk 2
3
7
11
15
Disk 3
P0
P1
P2
P3
Disk 4
Random writes in RAID 4
  Read the target block and the parity block
  Use subtraction to calculate the new parity block
  Write the target block and the parity block
RAID 4 has terrible write performance
  Bottlenecked by the parity drive
All writes must update the parity drive, causing serialization :(

## Slide 40: Analysis of RAID 4
Capacity: N – 1
  Space on the parity drive is lost
Reliability: 1 drive can fail
Sequential Read and write: (N – 1) * S
  Parallelization across all non-parity blocks
Random Read: (N – 1) * R
  Reads parallelize over all but the parity drive
Random Write: R / 2
  Writes serialize due to the parity drive
  Each write requires 1 read and 1 write of the parity drive, thus R / 2

## Slide 41: RAID 5: Rotating Parity
0
5
10
15
Disk 0
1
6
11
P3
Disk 1
2
7
P2
12
Disk 2
3
P1
8
13
Disk 3
P0
4
9
14
Disk 4
Disk 0 | Disk 1 | Disk 2 | Disk 3 | Disk 4
0 | 0 | 1 | 1 | 0 ^ 0 ^ 1 ^ 1 = 0
1 | 0 | 0 | 0 ^ 1 ^ 0 ^ 0 = 1 | 0
1 | 1 | 1 ^ 1 ^ 1 ^ 1 = 0 | 1 | 1
1 | 0 ^ 1 ^ 1 ^ 1 = 1 | 0 | 1 | 1
Parity blocks are spread over all N disks

## Slide 42: Random Writes and RAID 5
Random writes in RAID 5
  Read the target block and the parity block
  Use subtraction to calculate the new parity block
  Write the target block and the parity block
Thus, 4 total operations (2 reads, 2 writes)
  Distributed across all drives
0
5
10
15
Disk 0
1
6
11
P3
Disk 1
2
7
P2
12
Disk 2
3
P1
8
13
Disk 3
P0
4
9
14
Disk 4
Unlike RAID 4, writes are spread roughly evenly across all drives

## Slide 43: Analysis of Raid 5
Capacity: N – 1 [same as RAID 4]
Reliability: 1 drive can fail [same as RAID 4]
Sequential Read and write: (N – 1) * S [same]
  Parallelization across all non-parity blocks
Random Read: N * R [vs. (N – 1) * R]
  Unlike RAID 4, reads parallelize over all drives
Random Write: N / 4 * R [vs. R / 2 for RAID 4]
  Unlike RAID 4, writes parallelize over all drives
  Each write requires 2 reads and 2 write, hence N / 4

## Slide 44: Comparison of RAID Levels
 |  | RAID 0 | RAID 1 | RAID 4 | RAID 5
 | Capacity | N | N / 2 | N – 1 | N – 1
 | Reliability | 0 | 1 (maybe N / 2) | 1 | 1
Throughput | Sequential Read | N * S | (N / 2) * S | (N – 1) * S | (N – 1) * S
 | Sequential Write | N * S | (N / 2) * S | (N – 1) * S | (N – 1) * S
 | Random Read | N * R | N * R | (N – 1) * R | N * R
 | Random Write | N * R | (N / 2) * R | R / 2 | (N / 4) * R
Latency | Read | D | D | D | D
 | Write | D | D | 2 * D | 2 * D
N – number of drives
S – sequential access speed
R – random access speed
D – latency to access a single disk

## Slide 45: RAID 6
Any two drives can fail
N – 2 usable capacity
No overhead on read, significant overhead on write
Typically implemented using Reed-Solomon codes
0
4
8
P30
Disk 0
1
5
P20
P31
Disk 1
2
P10
P21
9
Disk 2
P00
P11
6
10
Disk 3
P01
3
7
11
Disk 4
Two parity blocks per stripe

## Slide 46: Choosing a RAID Level
Best performance and most capacity?
  RAID 0
Greatest error recovery?
  RAID 1 (1+0 or 0+1) or RAID 6
Balance between space, performance, and recoverability?
  RAID 5

## Slide 47: Other Considerations
Many RAID systems include a hot spare
  An idle, unused disk installed in the system
  If a drive fails, the array is immediately rebuilt using the hot spare
RAID can be implemented in hardware or software
  Hardware is faster and more reliable…
  But, migrating a hardware RAID array to a different hardware controller almost never works
  Software arrays are simpler to migrate and cheaper, but have worse performance and weaker reliability
    Due to the consistent update problem

## Slide 48
Hard Drives
RAID
SSD

## Slide 49: Beyond Spinning Disks
Hard drives have been around since 1956
  The cheapest way to store large amounts of data
  Sizes are still increasing rapidly
However, hard drives are typically the slowest component in most computers
  CPU and RAM operate at GHz
  PCI-X and Ethernet are GB/s
Hard drives are not suitable for mobile devices
  Fragile mechanical components can break
  The disk motor is extremely power hungry

## Slide 50: Solid State Drives
NAND flash memory-based drives
  High voltage is able to change the configuration of a floating-gate transistor
  State of the transistor interpreted as binary data
Flash memory chip
Data is striped across all chips

## Slide 51: Advantages of SSDs
More resilient against physical damage
  No sensitive read head or moving parts
  Immune to changes in temperature
Greatly reduced power consumption
  No mechanical, moving parts
Much faster than hard drives
  >500 MB/s vs ~200 MB/s for hard drives
  No penalty for random access
    Each flash cell can be addressed directly
    No need to rotate or seek
  Extremely high throughput
    Although each flash chip is slow, they are RAIDed

## Slide 53: Challenges with Flash
Flash memory is written in pages, but erased in blocks
  Pages: 4 – 16 KB, Blocks: 128 – 256 KB
  Thus, flash memory can become fragmented
  Leads to the write amplification problem
Flash memory can only be written a fixed number of times
  Typically 3000 – 5000 cycles for MLC
  SSDs use wear leveling to evenly distribute writes across all flash cells

## Slide 54: Write Amplification
Once all pages have been written, valid pages must be consolidated to free up space
Write amplification: a write triggers garbage collection/compaction
  One or more blocks must be read, erased, and rewritten before the write can proceed
Block X
Block Y
A
B
C
D
E
F
G
A’
B’
C’
D’
E’
F’
D’’
E’’
F’’
H
I
J
A’’’
B’’’
A’’
B’’
C’’
Stale pages cannot be overwritten or erased individually
G
K
L
G moved to new block by the garbage collector
Cleaned block can now be rewritten

## Slide 55: Garbage Collection
Garbage collection (GC) is vital for the performance of SSDs
Older SSDs had fast writes up until all pages were written once
  Even if the drive has lots of “free space,” each write is amplified, thus reducing performance
Many SSDs over-provision to help the GC
  240 GB SSDs actually have 256 GB of memory
Modern SSDs implement background GC
  However, this doesn’t always work correctly

## Slide 56: The Ambiguity of Delete
Goal: the SSD wants to perform background GC
  But this assumes the SSD knows which pages are invalid
Problem: most file systems don’t actually delete data
  On Linux, the “delete” function is unlink()
  Removes the file meta-data, but not the file itself

## Slide 57: Delete Example
File is written to SSD
File is deleted
The GC executes
  9 pages look valid to the SSD
  The OS knows only 2 pages are valid
Block X
Meta
Meta
File
File
File
File
File
File
File
Meta
Meta
File metadata (inode, name, etc.)
Metadata is overwritten, but the file remains
Lack of explicit delete means the GC wastes effort copying useless pages
Hard drives are not GCed, so this was never a problem

## Slide 58: TRIM
New SATA command TRIM (SCSI – UNMAP)
  Allows the OS to tell the SSD that specific LBAs are invalid, may be GCed
OS support for TRIM
  Win 7, OSX Snow Leopard, Linux 2.6.33, Android 4.3
Must be supported by the SSD firmware
Block X
Meta
Meta
File
File
File
File
File
File
File
Meta
Meta
TRIM

## Slide 59: Wear Leveling
Recall: each flash cell wears out after several thousand writes
SSDs use wear leveling to spread writes across all cells
  Typical consumer SSDs should last ~5 years

## Slide 60: Wear Leveling Examples
Block X
Block Y
A
B
C
D
E
F
G
A’
B’
C’
D’
E’
F’
D’’
E’’
F’’
H
I
G’
A’’’
B’’’
A’’
B’’
C’’
K
L
Wait as long as possible before garbage collecting
Block X
Block Y
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
M’
N’
O’
M’’
N’’
O’’
M’’’
N’’’
O’’’
M*
N*
O*
A
B
C
D
E
F
G
H
I
J
K
L
M*
N*
SSD controller periodically swap long lived data to different blocks
Blocks with long lived data receive less wear
If the GC runs now, page G must be copied
O*
Dynamic Wear Leveling
Static Wear Leveling

## Slide 61: SSD Controllers
All operations handled by the SSD controller
  Maps LBAs to physical pages
  Keeps track of free pages, controls the GC
  May implement background GC
  Performs wear leveling via data rotation
Controller performance is crucial for overall SSD performance
SSDs are extremely complicated internally

## Slide 62: Flavors of NAND Flash Memory
Multi-Level Cell (MLC)
One bit per flash cell
  0 or 1
Lower capacity and more expensive than MLC flash
Higher throughput than MLC
10000 – 100000 write cycles
Expensive, enterprise drives
Single-Level Cell (SLC)
Multiple bits per flash cell
  For two-level: 00, 01, 10, 11
  2, 3, and 4-bit MLC is available
Higher capacity and cheaper than SLC flash
Lower throughput due to the need for error correction
3000 – 5000 write cycels
Consumes more power
Consumer-grade drives